Calibration Information

| Spreader | Spread Width | Disc/Vane Type | Spreader Height (cm) | PTO/ Disk Speed | Vane Setting/ Drop On Point/ Discharge Point | Rate Setting 25kg/ha | Rate Setting 50kg/ha |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Accord HL | 24m | 285mm | 75 | 540 Disc 950 | Letter X | No.24-5 @ 12kph | No.42-3 @ 12kph |
| Amazone ZA-M 1000 | 18m | OM 10/18 | 100 | 540 | 90/76 |  | 10kph |
| Amazone ZA-U 1501 | 20m | Orange | 40.5 inches | 540 |  |  | 10kph |
| Amazone ZAM | 20m | OS 20-28 | 80 | 540 | 72/84 |  |  |
| Amazone ZAM | 20m | OM 18-24 | 80 | 540 | 22/44 | No.14 @ 10kph | No.19 @ 10kph |
| Amazone ZAM | 21m | OM 18-24 | 80 | 540 | 22/44 | No.15 @ 10kph | No.20 @ 10kph |
| Amazone ZAM | 21m | OS 20-28 | 80 | 540 | 72/84 |  |  |
| Amazone ZAM | 24m | OM 18-24 | 80 | 540 | 18/46 | No.17 @ 12.4kph | No.22 @ 12.4kph |
| Amazone ZAM | 24m | OS 20-28 | 80 | 540 | 68/86 | No.17 @ 12.4kph | No.22 @ 12.4kph |
| Amazone ZAM | 24m |  | 80 | 540 | 19/49 |  | No 21 @ 12kph |
| Amazone ZAM | 24m | OM 24-26 | 80 | 540 | 19/49 |  | No.21 @ 12kph |
| Amazone ZAM | 28m | OM 18-24 | 80 | 540 | 22/50 |  |  |
| Amazone ZAM | 28m | OS 20-28 | 80 | 540 | 72/90 |  |  |
| Amazone ZAM | 36m | OM 24-36 | Level | 1200 @ 520 | 20/50 | N/A | N/A |
| KRM F2 | 24m | 6 vane | 80 + 2o tilt | 900 | D.O.P. 4 |  | 10kph |
| KRM L2plus | 24m | E2T | 75 + 2* tilt | 540 | Pos 1 + 2 | No.1.5 @ 12kph | No.19 @ 12kph |
| KRM M2 | 24m | E2T | 75 + 6* tilt | 540 | Pos 1 + 2 | N/A | N/A |
| KRM M2 | 36m | E8T | 75 + 2* Tilt | 540 | Pos 1 + 2 | N/A | N/A |
| Kuhn ZSB | 12m | Standard | 75 level | 540 |  | No.10 @ 10.2kph |  |
| Kuhn MDS 701 | 12m | M1 | 50 | 540 | C3/A3 |  | 11kph |
| Kuhn MDS 1141 | 18m | M3 | 120 | 540 | E6/D5 | No.20 @ 15kph | No.40 @ 15kph |
| Kuhn MDS 1141 | 24m | M5 | 50 | 540 | E5/B2 | N/A | No. 36 @ 10km/h |
| Kuhn Axis 20.1 | 20m | S4 | 60 | 540 | DOP 3.5 | N/A | N/A |
| Kuhn Axis 30.1 | 21m | S4 | 50 | 540 |  | No.6 @13kph |  |
| Kuhn Axis 30.1 | 24m | S4 | 50/50 | 540 | 7 |  | No. 32 @ 12 kph |
| Kuhn Precis K 1100M | 24m | D4 | 50 to frame | 540 | No.3 | No.11 @ 10kph | No.18 @ 10kph |
| Kuhn Axis | 30m | S4 | 50 | 600 | D.O.P. 9 |  | 16kph |
| Kuhn Axera H 1102 EMC | 36m | D4H | 80 level to the disc | 1150 disc | No.9 | N/A | N/A |
| Lely Centreliner | 18m | Standard | 75 +2o tilt | 540 |  |  |  |
| Spalding Super Vario | 6m | Standard | 90 | 850 | 4.5 | No.45 @ 13kph |  |
| Sulky DPX 1154 | 12m | 18/28 | 75 | 540 | D.O.P. 2.3 |  | 10.5kph |
| Sulky DPX Expert | 20m | 18/24 | 75 | 540 | 145 | Reduction slides fitted, lowest setting @ 12kph |  |
| Vicon RSM | 12m | 135,185, 235mm | 75 | 540 | Letter M | No.13 @ 10kph | No.18 @ 10kph |
| Vicon RSL | 20m | 6 Vane | 75/75 | 540 | D.O.P L |  | 12kph |
| Vicon RSM | 21m | 185,235, 285mm | 75 | 540 | Letter G |  |  |
| KRM Bredal K65 | 18 m | A Disc | 80 | 650 |  |  |  |

Where there is N/A in the Rate Setting column this indicates the machine tested was self-calibrating.

Settings provided in the spreading table above are derived from practical tests in the field carried out by SCS Spreader & Sprayer Testing Ltd.

All of the spreaders used for the tests have been checked by an SCS engineer to ensure that they are in good working order. Any spreaders not in such condition can have a detrimental effect upon the spread patterns, which may cause visible problems in the field.

All settings given as a guide only, no liability will be accepted for any loss or damage to the spreader or crop loss arising as a result of the services provided except in so far as such damage results from the negligence or breach of statutory duty of the SST engineer. In any case SST liability shall not in any circumstances exceed the sum equal to the amount of SST charges in respect of the relevant transaction.